## Slide 1: Air Practitioners Meeting
Selected Practitioners Comments to New O. Reg. 419/05 Guidance Documents

## Slide 2: Practitioners Response and Comments
ESDM Guide: Appendix B, Table B‐3:
  MOECC proposes to remove:
    maintenance welding operations;
    standby power generators;
    natural gas fired equipment with a total facility wide heat input less than 20 million kJ/hr; and,
    low temperature handling of compounds with a vapour pressure less than 1 kPa;
  All of the emission sources that the MOECC proposes to remove from Table B‐3, should remain.

## Slide 3: Practitioners Response and Comments
ESDM Guide: Appendix B, Table B‐3:
  By removing the emission sources from Table B‐3, industry would have to provide even more detailed calculations to demonstrate negligibility.
  This would be burdensome and low value work for industry on emissions that are negligible and this information would provide little value to the MOECC.

## Slide 4: Practitioners Response and Comments
ESDM Guide: Appendix B, Table B‐3:
  Reviewing negligible emission calculations definitely will not speed up the MOECC’s review of ECA applications.
  We understand that there has been “abuse” in using this table, but the exceptions should be dealt with through further guidance.
  MOECC always has the opportunity to ask for further information when warranted.

## Slide 5: Practitioners Response and Comments
ESDM Guide: Appendix B, Table B‐3:
  MOECC proposes to remove:
    sources that are exempt from obtaining a C of A.
  It is not clear if this is intended:
    as an obvious change because sources that do not need to be included in an ESDM; or,
    That even sources that are exempt need to be assessed for significance in the ESDM.

## Slide 6: Practitioners Response and Comments
ESDM Guide: Appendix B, Table B‐3:
  If the former, clarification should be provided in the guidance document.
  If the latter, we strongly suggest this be reconsidered. Extraordinary efforts and costs are incurred in assessing insignificance of minor sources.

## Slide 7: Practitioners Response and Comments
ESDM Guide: Section 6.1.1
  There is still a challenge with the “inclusive” list. There are very small facilities that fit these NAICs codes that do not have storage piles, open handing, or “on‐site” roads.
  These are small facilities that can be part of an industrial strip mall and only have shared parking. Some discussion should be provided that these types of smaller facilities to not need a fugitive dust plan. This situation will only be exacerbated by the inclusion of the “other miscellaneous”.

## Slide 8: Practitioners Response and Comments
ESDM Guide: Section 7.4
  The “such as” list should be expanded.
  At present, ONLY stockpiles and roadways are considered exempt if a Best Management Plan is available. All other fugitive sources are still required to be modelled.
  It would be very helpful if other difficult to model sources such as bull dozing, grading and material handling were also considered.

## Slide 9: Practitioners Response and Comments
ESDM Guide: Section 7.4 (continued)
  This is especially significant in that the BMP requirements are for ALL fugitive sources, not just roadways and stockpiles.
  The requirements should also be very clear that this addresses on‐site roads managed by the facility.
  In some cases BMPs have been required for parking lots shared with other facilities. (see comment above on Section 6.1.1.).

## Slide 10: Practitioners Response and Comments
ESDM Guide: Section 9.2
  Full compliance testing done as a condition of an ECA under maximum operating conditions should be accepted as “highest data quality”.
  This type of compliance testing would be considered “above average”.
  Current approach could allow for a fully compliant test under an ECA to be deemed “noncompliant” under O.Reg. 419 if a higher emission rate was available from other sources or approaches.

## Slide 11: Practitioners Response and Comments
ESDM Guide: Section 9.2 (continued)
  Mass balance.
    Under the “highest data quality”, it states that mass balance “may” be considered highest data quality, but under “above average quality” it states that mass balance “can” be considered above‐average.
    Both mass balance approaches are exactly the same.
    It is not clear why there are differences and when different data quality applies.

## Slide 12: Practitioners Response and Comments
ESDM Guide: Section 9.2 (continued)
  “Validated” source testing.
    It is not clear what the difference is between validated source testing and partially validated source testing.
    The “partially’ validated testing would seem to imply that this is consistent with compliance testing for an ECA.

## Slide 13: Practitioners Response and Comments
ESDM Guide: Section 12.2
  Blue box, page 79 “for each contaminant with no Ministry POI limit”.
  Add the word significant in front of contaminant.
  Some contaminants can be screened out using threshold calculations.

## Slide 14: Practitioners Response and Comments
ESDM Guide: Page 100
  Guidance for welding operations – note that maintenance welding has been removed from the table B‐3 (though we want it back in).
  Also, the links to approximating isocyanate emissions are no longer valid.

## Slide 15: Practitioners Response and Comments
ESDM Guide: Page 106 (Checklist)
  Section 5, SST – should be clear that the source summary table is in one format or the other, and that we’re not expected to provide both.
  Different review engineers have expressed preferences for either contaminant based or source based.
  It should be clear that either is acceptable.

## Slide 16: Practitioners Response and Comments
ADMGO: Section 7.3
  The text indicates that MOECC will require an assessment using SCREEN3 to see if shoreline effects could occur if a source is within approximately one km of a major water body.
  The text goes on to state that if there are possible shoreline effects, a facility must then go to MOECC to use a different model for compliance assessment.

## Slide 17: Practitioners Response and Comments
ADMGO: Section 7.3
  The SCREEN3 requirement and using an alternate model for compliance is totally against the “approved model” and “tiered model” approach established in O. Reg. 419 where a facility demonstrates compliance with the approved models and met data.
  A facility doesn’t need to demonstrate compliance with all of the approved models or be found out of compliance by picking another approved model or approved met set.

## Slide 18: Practitioners Response and Comments
ADMGO: Section 7.3
  Adding the shoreline assessment and requirement to use an alternate model violates the basis of O.Reg. 419.

## Slide 19: Practitioners Response and Comments
ADMGO: Section 11.2
  Public roadways between two parcels of the same facility are not considered points‐of‐impingement.
  We recommend that adjacent road ways as well as utility corridors be treated in the same way (i.e. not be considered as points of impingement).
  For clarity also include facades of high‐rise buildings at locations where there are no intakes or openings to the building.

## Slide 20: Practitioners Response and Comments
GIASSO: page 12
  Note indicates that Schedule 5 facilities must use the Reg 346 model.
GIASSO: page 73
  Percentiles plots could be considered a tool and are easily generated in AERMOD (i.e, max at 99.9%, 99.5% etc) to show frequency and magnitude of exceedance

## Slide 21: Practitioners Response and Comments
Guide to Requesting a Site-Specific Std.
  There is a lot of duplication between this and GIASSO. This could be an Appendix to GIASO.
  The document uses the term “exposure” in numerous places as a broad statement in relation to limiting or reducing emissions to air.
    O.Reg 419 only deals with emissions from a specific facility and does not deal with cumulative exposure or background levels.
    The document should be specific to indicating site specific or technical standards only deal with emissions and point‐of‐impingement concentrations from a specific facility.